## Slide 1
Three – Way
&
Four – Way Switches
PowerPoint Created by:
Sidney Bell
Area Ag. Mechanics Teacher
North Region Agricultural Education

## Slide 2
Three Way Switches
Single Pole Double Throw
(SPDT)
Traveler Terminals (Usually Silver)
Common Terminal
(Usually Black)
Also called
Hinge Terminal

## Slide 3
Rules for Three-Way Switches
Three-Way Switches are used in pairs
Must use three conductor cable between the switches
Power (source conductor) enters the common (hinge) terminal on one three-way switch
Power leaves the common terminal of the other three-way switch and goes to the switched outlet
Traveler conductors attach to the traveler terminals

## Slide 4
Source Conductors
COMMON
COMMON
Double Throw because the switch will close in two positions
Single Pole because it will “break” only one ungrounded conductor
Toggle DOWN
Toggle UP
ON
OFF
Toggle UP
Toggle UP
Toggle DOWN
ON

## Slide 5
Light-Switch-Switch
(Light Controlled by Two Three-Way Switches)
S3
S3

## Slide 6
Ladder Diagram for a light controlled by a Three – Way Switch

## Slide 8
Switch- Light - Switch
(Light Controlled by Two Three-Way Switches)
S3
S3

## Slide 10
Four – Way Switch
(Double Pole Double Throw)
A
D
C
B
Horizontal terminal configuration paired terminals are horizontal
AB pair
CD pair

## Slide 11
A
D
C
B
Four – Way Switch
(Double Pole Double Throw)
Horizontal terminal configuration paired terminals are horizontal
AB pair
CD pair

## Slide 12
Rules for Four-Way Switches
  Three – Way switch rules apply
  Four – Way switch must be used between two Three - Way Switches
  Traveler conductors from one three – way switch must connect to one “pair” of the traveler terminals on the four – way switch
  Traveler conductors from the other three – way switch will connect to the other “pair” of traveler terminals on the four – way switch

## Slide 13
S3
S3
S4