## Slide 1
Drawing
Electrical Circuits in
Power Point

## Slide 2
S
S4
S3
20 Ampere
240 volt 2 pole 3-wire grounding type receptacle
LINE
LOAD
TEST RESET
GFCI
P

## Slide 3
Black insulated = ungrounded conductor “HOT”
Red insulated = ungrounded conductor “HOT”
White insulated = grounded conductor “NEUTRAL”
Green insulated or Bare Copper = Equipment ground or “Grounding” conductor. Normally non-current carrying conductor. Transmits current to the earth in the event of an electrical short circuit

## Slide 4
Service Entrance Panel (SEP)
Electrical Symbols
Ceiling Outlet
Fluorescent Fixture
S
GFCI
P
Single Receptacle Outlet
Duplex Receptacle Outlet
Duplex Receptacle Outlet
(split wired)
Switched Convenience Outlet
Ground Fault Circuit Interrupter
GFCI Protected Outlet
Lighting Outlets
Receptacle Outlets
Switch Outlets
S Single Pole Switch
S2 Double Pole Switch
S3 Three-Way Switch
S4 Four-Way Switch
Motor Switch
M
Service Entrance Panels
For more Information on Electrical Symbols:
AAVIM Electrical Wiring
AAVIM Electrical Controls
Rural Electricity Resource Councils Agricultural Wiring Handbook

## Slide 5
Drawing Tools in Power Point

## Slide 6
Floor Plan: Indicates how conductors should be sourced

## Slide 7
Basic Rules for Wiring Circuits
1. The grounded conductor (white) must travel uninterrupted from any device where current is utilized, back to the source (service entrance panel)
2. Grounded conductors connect to silver or white terminals on devices.
3. Ungrounded “Hot” conductors (black, red) attach to brass or black terminals.
4. Manual toggle switches do not require grounded “Neutral” conductors.
5. Power enters a single pole toggle switch by means of an ungrounded conductor on one terminal and leaves the switch by means of an ungrounded conductor on the other terminal.
6. Do not connect an ungrounded conductor directly from the source (circuit breaker) to a lighting device unless it is intended to be “Hot” at all times.
7. Metal boxes must be “bonded” or grounded to the earth by means of a grounding conductor and grounding type devices must be grounded by means of a grounding conductor.

## Slide 9
S
120 V circuit: Light controlled by single pole switch.
60 Watt

## Slide 11
S
120 V circuit: Light controlled by single pole switch.
60 Watt

## Slide 13
S
60 Watts
120 V circuit, duplex receptacle and a light controlled by a single pole switch

## Slide 15
S
60 Watts
1400 Watts
120 V circuit, duplex receptacle and a light controlled by a single pole switch. Circuit expected to run continuously for 6 hours/day.
NEC 210.20(A): Where a branch circuit supplies continuous loads or any combination of continuous and noncontinuous loads, the rating of the overcurrent device shall not be less than the noncontinuous load plus 125 percent of the continuous load.
W =VA
1400 Watts + 60 Watts = 1460 Watts ÷ 120 V = 12 .166 Amps X 1.25 = 15.2 Amps
Circuit requires 20 Amp overcurrent protection and 12 AWG conductor.
Determine box size based on 12 AWG conductor!

## Slide 17
S
60 Watts
1300 Watts
120 V circuit, duplex receptacle and a light controlled by a single pole switch.

## Slide 19
Tips on how to use this tutorial
Share this Power Point with students by email and provide them with specific instructions regarding what circuits you would like for them to diagram
Have students save their diagrammed circuits by clicking file, save as, adding their name at the beginning of the file name, saving it to their desk top or files then attach and send it to you via email or follow your schools procedure for saving to Google Drive and sharing with their teacher.
If you want students to try more advanced circuits, download the Drawing Intermediate Electrical Circuit Power Point from the Ag. Ed. Website by clicking on the link provided.