Course:	01.431		Agriculture Crop Production and Management

Unit 4:		Soil Practices

Lesson 2:		Land Classification and  Use

QCC:	343, 349, 354

Objectives:

1.	Explain the features and uses of land.

2.	Describe land capability and list capability factors.

3.	Perform land capability classification.

Teaching Time:

4 hours

References:

Biondo, Ronald J. & Jasper S. Lee. Introduction to Plant and Soil Science and 		Technology. Interstate Publishers, Inc. Danville, IL 1997.

Materials and Equipment:

Land lab

Field trip

Soil samples for texture

Teaching Procedure

Introduction and Mental Set

Ask student why one parcel of land would sell for a higher price than another.  Also, what limits the use of a particular parcel of land?

A land classification is a group we put land in after evaluating characteristics.  There are 8 land classifications.

Discussion

1.	What is land?

Natural and artificial characteristics of an area to be used for agricultural or other purposes.

2.	What are the uses of land?

A.	Crops, buildings, houses, streets, roads, schools, recreation, wetlands, and Forestry.

B.	Land Classes 1-4 -used primarily for the production of crops.

C.	Class 5-best suited for pasture or Forestry, usually wet or flooded parts of the year or has rock outcrops.

D.	Class 6-best suited for pasture, Forestry, wildlife habitat, watershed areas, and recreation due to the extreme slope

E.	Class 7-has severe limitations-extreme slopes, shallow, soil best suited for forestry, pasture, wildlife habitat, recreation, and watershed areas.

F.	Class 8-Unsuited for plant production-swamps or mountains-used basically for recreation

3.	Discuss the concept of cropland.

Land used to grow crops-only classes 1-4 are classified use to grow crops.  Southern Georgia is the primary area of the state used for cropland.  Usually because of the terrain of the soil and the availability of water

4.	What are the characteristics of cropland?

The major characteristics of cropland include: soil type, climate, topography, water, subsurface factors, and pollution-p. 138-139

5.	Tell students how each of these will affect cropland use.

A.	Soil type:  include soil texture, nutrients and internal structure all influence soil productivity

B.	Climate:  Average weather conditions over a long period of time can determine which crops and be grown and what time of year they can be effectively grown.

C.	Topography:  the form or outline of the surface of the earth.  Slope or terrain affect type of vegetation that can be grown

D.	Water supply:  the most limiting factor that affects cropland use.  Limited water greatly determines type of crop or crops that can be grown.

E.	Subsurface factors:  such as drainage, shallow rock or hardpans can adversely affect cropland.

F.	Pollution:  Land may be polluted an unsuitable for crop production though all other factors are favorable.

6.	What is land capability?

The suitability for agriculture uses.

A.	Define arable land and discuss with students

- Arable land is land that can be used for row crops that typically require some tillage, Arable land can be tilled and is where crop production is practiced

7.	How can land be improved? (p. 141)

A.	Irrigation

B.	Erosion control

C.	Drainage

D.	Forming

8.	Discuss the capability factors of soils.

A.	Texture; % sand, silt, clay; how it feels

B.	Drainage; how fast water moves through the soil

C.	Soil Depth; depth of topsoil

D.	Erosion; topsoil loss by wind, water

E.	Slope; rise and fall (refer to worksheet ADetermining Slope@)

F.	Runoff; water that does not soak in

See text pp. 143-145 for detailed explanation of each above

9.	What does some of the land in our area look like?

A.	Write descriptions on board, rate the land described from best to worst

B.	Using land capability classification system pp. 145-150, classify the rated land.

10.	Activities

A.	Take students out to land lab or field trip and determine various areas of land capability classification.

B.	Review main ideas with students.  Have students complete questions and define terms for unit.

Summary

Land is used for various things.  Some land is better suited for agriculture than other areas.  We need to remember that the best land should be used for agriculture if we are to continue to be productive.

Evaluation

Fill out land evaluation card

Written test

DETERMINING SLOPE

A.  Basic Understandings

- To be successful in determining a land class, you must be able to determine the slope of the land.  In many cases, the land class will be determined primarily by slope.  In the FFA Land Judging Career Development Event, contestants must determine slope without the use of any instrument.  With practice, a person can accurately estimate the slope of land.

- Slope is defined as the angle of inclination from the horizontal.  In other words, slope is the amount of deviation from the horizontal position.

- Slope is expressed in percent.  The slope will be determined by the number of feet of rise or fall (measured vertically) in 100 feet of horizontal distance.

In this example, point A and point B are 100' apart, measured horizontally. The vertical height between point A and point B is 12'.  Thus, feet of rise from point A to point B is 12'.  Likewise, the feet of fall from point B to point A is 12'.  Therefore, the slope is:

12'      100' = .12 = 12% slope.

B.  Classes of Slope

1.  There are seven classes or categories of slope.

2.  Slope classes are identified by a letter and category based upon the percentage of slope.

- Slope classes in north Georgia differ from the classes in south Georgia.  In a Land Judging Career Development Event, the slope classes that are appropriate for the area of the state in which the event is held will be used.

- Slope classes are:

| SLOPE CLASS | PERCENTAGE SLOPE NORTH GEORGIA | PERCENTAGE SLOPE SOUTH GEORGIA |
| --- | --- | --- |
| A - NEARLY LEVEL | 0 - 2% | 0 - 2% |
| B - VERY GENTLE | 2 - 6% | 2 - 5% |
| C - GENTLE | 6 - 10% | 5 - 8% |
| D - SLOPING | 10 - 15% | 8 - 12% |
| E - STRONGLY SLOPING | 15 - 25% | 12 - 17% |
| F - STEEP | 25 - 60% | OVER 17% |
| G - VERY STEEP | OVER 60% | NOT APPLICABLE |

C.  Effect of Slope on Land Classification

1.  When classifying land, slope will often be the factor that determines the land class.  While other soil factors will also affect the land class, the better soils are usually classified based on the slope.

- There is a best possible land class for each slope category:

| SLOPE CATEGORY | BEST POSSIBLE LAND CLASS |
| --- | --- |
| A - NEARLY LEVEL | I |
| B - VERY GENTLE | II |
| C - GENTLE | III |
| D - SLOPING | IV |
| E - STRONGLY SLOPING | VI |
| F - STEEP | VII |
| G - VERY STEEP | VII |

D.  Estimating Slope

- When participating in the FFA Land Judging CDE, contestants must estimate the slope.  No instrument may be used to measure the slope.  With practice, a person should be able to estimate slope accurately.

- When estimating slope, a student must be able to visualize two lines.  Using an actual field situation and the example that follows, instruct the students on how to visualize these two lines that will help them estimate slope.

a.  First visualize a horizontal line from the ground level at the up slope stake(slope stake B) toward the other slope stake.  Remember that the slope will be the deviation from this horizontal line.

b.  Next, visualize a vertical line from ground level at the down slope stake                 (slope stake A) upward to the imaginary horizontal line.

c.  The slope for the field will be the length of the vertical line.

- A demonstration such as the one that follows may help students visualize slope estimation.  The following equipment is needed for this demonstration:

-Two slope stakes 100 feet apart

-Piece of heavy string (twine) at least 100 feet long

-Line level

-10' length of 1-1/2" PVC pipe.  The pipe should be marked in one foot increments.  The pipe should be also painted different colors to      represent the different slope classes.  (0 - 2' should be painted a color, 2' - 6' should be a different color, 6' - 10' should be another color)

Set up the demonstration as follows.

a.  Attach one end of the string to the bottom of the upper slope stake (slope        stake B) so that the string will be at ground level.

b.  Attach the line level to the string.

c.  Have someone hold the PVC pipe at the lower slope stake (slope stake A).

d.  Hold the loose end of the string against the PVC pipe.  Move string up or                   	down until the line level indicates that it is level.

e.  Read the number of feet on the PVC pipe which will be the slope.

f.   Point out the slope class (A, B, or C) as indicated by the painted area on    	    	 the PVC pipe where the string is located.

- As the demonstration on slope estimation is conducted, point out to the students that they must be able to visualize the string and the measurement up to the string.  It should help the students in estimating the measurement to be able to accurately estimate a vertical measurement such as 3 feet, 5 feet, or 6 feet.  They should practice estimating the measurement  that they will work with.  When they can accurately estimate this measurement, they can more accurately determine how many 3' or 5' measurements there are from the base of lower slope stake up to the imaginary horizontal line.

E.  Measuring Slope

- Even though students will not be able to use any instrument to measure slope, obviously the teacher must be able to accurately measure the slope when teaching slope estimation.

- When properly used, a transit or farm level and surveyor rod will be the most accurate method of measuring slope.  However, more time is required in measuring slope in this manner because of the time required to set up the instrument each time the instrument is moved.  It is recommended that instruction be given in the use of transits and/or levels since this also helps to give a better understanding of slope and differences in elevation.  Refer to following pages.

- A clinometer can also be used to measure slope.  Clinometers are often used to measure tree heights.  Therefore, many agricultural education departments will have one or more of these instruments.

a.  There are a number of different versions of

clinometers available.  The clinometer will                                  have two different scales.  One scale is a

percent scale.  The other scale is usually a

topographic or degree scale.  Clinometers

differ as to which scale is on the right and

which scale is on the left.  When using the

clinometer to determine slope, be sure to

use the percent scale.  If you are not sure

which scale is the percent scale, tilt the

clinometer until you can see the end of the

scale.  The percent scale is usually indicated

at the end of the scale.  On some clinometers,

the percent scale is also indicated near the

A0" mark.

b.  How to hold and read a clinometer

(1) When reading the percent scale, position yourself 100 feet from the                           		target.

(2) Keep both eyes open when using the clinometer.

(3) Use one eye to look through the lens at the scale while the other eye                         		sights along the clinometer housing.

(4) An optical illusion is created and the horizontal sighting line inside the                       		clinometer appears to project outside the housing.

(5) Place this sighting line on the target and read the scale.

c.  There are several methods that can be used to measure slope with a                         		clinometer.  The method described is only one such method.

(1) A target is needed 100' away to take a reading.  An easy way to make a target is 		to mark a rod or pipe or similar object at your eye level.  To do this, stand on a 		level surface and have someone hold a rod or pipe near you.  The rod or pipe 			should be held plumb.  Look through the lens of the  clinometer and sight on the 	A0@ mark.  The sighting line should appear to be on the outside of the clinometer.  	Have the person holding the target move his/her finger up or down on the target until 	the finger lines up with the A0" mark in the clinometer.  Mark this point on the rod or 	pipe with tape or in some other way so that you can see the mark from 100 feet apart. 	 Use the marked rod or pipe as the target when measuring slope.

(2) To measure slope, measure 100 feet either up slope or down slope. Since you have 	a target that is eye level, it will make no difference which way the slope is measured.  	Have someone hold the target plumb at the 100' mark.  Align the sighting mark in the 	clinometer with the mark that is on target.  Read the percent scale.  The reading that you 	get will be the slope.

- Another method of measuring slope is the 100 inch board method.  This method is fairly accurate if the slope is uniform.

Figure 21-4:   Determining Per Cent of Slope.  The yardstick shows the distance between the bottom of the leveled, woo inch board and the ground.  This vertical distance in inches is equal to the slope of the ground in per cent

F.  Adjustments to Slope When Measurement is Not Made at 100 Feet

Remember that slope is expressed in percent and is determined by the number of vertical feet rise or fall in 100 feet of horizontal distance.

In the FFA Land Judging CDE, the slope stakes are usually set 100 feet apart.  However, sometimes the slope stakes may be some distance other than 100 feet apart.  If the slope stakes are not set 100 feet apart, the distance will be included on the assumption card, or the field monitor will tell contestants the distance between the stakes.

If the slope stakes are not 100 feet apart, adjustments must be made in the vertical difference between the stakes.  If the slope stakes are not 100 feet apart, determine the slope by dividing the vertical distance by the distance between the slope stakes.  Explanation:

a. Slope is expressed as a percentage.

b. If the vertical rise or fall is 12 feet in 100 horizontal feet, the slope         will be   12   100 = .12 = 12%.

c. If the vertical rise or fall is 12 feet in 50 horizontal feet, the slope                                	will be    12   50 = .24 = 24%.

d. If the vertical rise or fall is 12 feet in 75 horizontal feet, the slope                               	 will be     12   75 = .16 = 16%.

SPECIAL NOTE:

If a clinometer is used to measure the slope using the method described, 	do not make an adjustment to the slope reading if the slope is measured at a distance other than 100 feet.  While it is best to use the clinometer at a distance of 100 feet to compensate for any variations in the slope, it can be used at other distances to read the slope, and the reading will be the same (if the slope is uniform).  If the method described is used to measure slope with a clinometer, the reading that you get will be percentage, not feet.  Therefore, no adjustment to the reading is needed.

You can convert the percentage to feet by multiplying the percentage by the number of feet that you are standing from the target.  Example:

The percentage reading at 100' is 8%.  Vertical measurement in feet =

.08 x 100' = 8 feet.

The percentage reading at 50' is 8%.  Vertical measurement in feet =

.08 x 50' = 4 feet.