Unit 7

Servicing Horticultural Equipment

Pre/Post Test

Directions:  For questions 1 – 18, select the best answer.

- Hand held string trimmers have _____ cycle engines.

a.  2		b.  4

c.  6		d.  8

- A term referring to the oil’s thickness is:

a.  lubricant	b.  balance

c.  viscosity	d.  proportion

- What tool is used to check the gap of a spark plug?

a.  hammer		b.  screw driver

c.  socket wrench	d.  feeler gauge

- When the air temperature is above 40 degrees Fahrenheit, Briggs and Stratton recommends using _____ weight oil.

a.  10		b.  20

c.  30		d.  40

- When storing a small engine, what is added to the spark plug cylinder?

a.  diesel fuel	b.  gasoline stabilizer

c.  oil		d.  ether

- When storing a small engine, what is added to the gasoline?

a.  diesel fuel	b.  gasoline stabilizer

c.  oil		d.  ether

- Fuel for small engines should be used within _____ days.

a.  15		b.  20

c.  25		d.  30

- Under normal conditions, air filters need servicing every _____ months or every 25 hours of operation.

a.  2		b.  3

c.  4		d.  5

- What is the proper spark plug gap?

a.  .030 inch	b.  .040 inch

c.  .050 inch	d.  .060 inch

- How often should the oil level be checked?

  - every time the fuel tank is filled

  - once a month

  - every other month

  - once a year

- A two cycle engine has two cycles.  One cycle is a compression stroke.  What is the other stroke?

a.  depression	b.  power

c.  balance		d.  scale

- A two cycle engine must have _____ mixed with gasoline for efficient operation.

a.  oil		b. water

c.  baking soda	d.  ether

- Before working on a small engine, what should be disconnected to prevent accidental starting?

a.  blade		b.  spark plug

c.  wheel		d.  dipstick

- On a new engine, the first oil change should occur after the engine has operated for _____ hours.

a.  10		b.  20

c.  30		d.  40

- Under normal conditions, the oil should be changed after _____ hours of operation or once a month.

a.  30		b.  40

c.  50		d.  60

- Where should the old oil be placed after changing?

a.  local oil recycling center	b.  in the river

c.  around an ant mound		d.  around a tree

- To change the oil, the engine needs to be:

a.  warm		b.  cold

c.  running		d.  warm or cold

- Under normal conditions, the spark plug should be replaced after _____ hours of operation.

a.  50		b.  75

c.  100		d.  125

Directions:  For questions 19 - 20, write the correct responses.

- When sharpening a mower blade, what safety equipment is needed?

- What are three advantages of maintaining a small engine?