# Course:	01.423		Agriculture Mechanics Technology III

Unit 7:	Plumbing

Lesson 2: Plumbing Maintenance and Repair

Georgia Performance Standards: 	  AG-AMII-7 (e-h)

Academic Standards: SPS7, ELA12LSV1, ELA9RL5, ELA10W3, MM1A3, MA1P1, MA1P3, SCSh2, SCSh3, SCSh4, SP1, SPS5, ELA9RC2

Objectives:

1.	Replace worn or broken seals.

2.	Maintain pumping source.

3. 	Maintain control systems.

4.	Maintain drainage lines.

Teaching Time: 5 hours

Grades: 9-12

Essential Question: How do you maintain and repair plumbing?

Unit Understandings, Themes, and Concepts:

Students will gain an understanding of how to maintain and repair plumbing.

Primary Learning Goals: Students will be able to perform various tasks necessary in maintaining and repairing plumbing.

Students with disabilities: For students with disabilities, the instructor should refer to the individual student's IEP to insure that the accommodations specified in the IEP are being provided within the classroom setting. Instructors should familiarize themselves with the provisions of Behavior Intervention Plans that may be part of a student's IEP. Frequent consultation with a student's special education instructor will be beneficial in providing appropriate differentiation within any given instructional activity or requirement.

Assessment Method/Type:

____ Constructed Response		____ Peer Assessment

_X__ Combined Methods		____ Selected Response

____ Informal Checks			____ Self Assessment

References:

Cooper, Elmer L.  Agricultural Mechanics Fundamental & Applications, 2nd ed.  Delmar Publishers Inc. Albany, NY. 1992

Burke, Stanley R. and T. J. Wakeman.  Modern Agricultural Mechanics, 2nd ed.  Interstate Publishers, Inc. Danville, IL. 1992

Materials and Equipment:

Faucet, O-ring, faucet packing, washers, seat, diaphragm, float valve, flush valve, water tank

Web Resources:

PowerPoints:

Georgia Performance Standards: AG-AMIII-7 (e-h)

AG-AMIII-7:  Students will demonstrate proper plumbing techniques.

e.      Replace worn or broken seals.

f.	Maintain pumping source.

g.	Maintain control systems.

h.	Maintain drainage lines.

Academic Standards:

ELA9RC2 The student participates in discussions related to curricular learning in all subject areas.

ELA12LSV1 The student participates in student-to-teacher, student-to-student, and group verbal interactions.

ELA9RL5 The student understands and acquires new vocabulary and uses it correctly in reading and writing.

ELA10W3 The student uses research and technology to support writing.

MM1A3. The student solves simple equations.

MA1P1. The student solves problems (using appropriate technology).

MA1P3. The student communicates mathematically.

SCSh2 The student uses standard safety practices for all classroom laboratory and field investigations.

SCSh3 The student identifies and investigates problems scientifically.

SCSh4 The student uses tools and instruments for observing, measuring, and manipulating scientific equipment and materials.

SP1 The student analyzes the relationships between force, mass, gravity, and the motion of objects.

SPS5 The student compares and contrasts the phases of matter as they relate to atomic and molecular motion.

SPS7 The student relates transformations and flow of energy within a system.

Teaching Procedure

Introduction and Mental Set

Ask students to share with the class their remedies for maintaining their water system at home.  You will get a variety of answers, some good and some not so good.  These will give you a general idea as to the types of water problems the students are facing.

I.  Discussion

1.	What causes faucets or valves to leak?

A.	Certain types of water.

2.	Discuss the make up of:

A.	Faucet

- O ring

- Packing

- Washer, faucet

- Seat

- Diaphragm

B.	Valve

- Float valve

- Flush valve

3.	List the procedure in replacing a washer in a faucet.

A.	Shut off the water supply.

B.	Unscrew the packing nut and spindle.

C.	Remove the spindle.

D.	Remove the washer, retaining the screw that you see on the end of the spindle.

E.	Replace the worn washer with the proper-sized new one.

F.	Tighten the retaining screw.

G.	Replace the spindle, and then tighten the packing nut.

H.	If the faucet continues to leak, consider replacing it.

I.	Turn water back on.

4.	List the procedure in stopping the leakage around the stem.

A.	Shut off the water supply.

B.	Tighten the packing nut (In many cases, simply tightening the packing nut may stop leaking).

C.	If packing is worn or hard, it should be replaced with new valve-stem packing.

D.	Unscrew the packing nut from the body of the faucet or valve, and then wrap the packing tightly around the stem.

E.	Replace and tighten the packing nut.

F.	Turn water back on.

5.	List the procedures in repairing a float valve assembly.

A.	Tighten the nut or replace a gasket to stop leaks at the point where the assembly passes through the bottom of the tank.

B.	A washer or diaphragm in the valve may need to be replaced to stop a flooding condition caused by the valve not shutting off completely.

C.	Some systems use a hollow ball for a float.  If the ball develops a leak, it will fill with water and no longer float.  In this case, the float and its rod are unscrewed from the assembly and replaced.

6.	List the procedures in repairing a flush valve.

A.	In most cases the problem is caused by the chain or linkage getting twisted or caught on another part.

B.	This can be corrected by simply flipping the trip level up and down.

C.	If this does not permit the valve to reseal, then the flapper or ball seal and other parts should be cleaned of all rust, slime, or other deposits.

D.	If this does not correct the problem, replace the flapper and other parts as required.

II.  Activities

A.	The student will repair a faucet that leaks at the stem.

B.	The student will repair a dripping faucet.

- The student will repair a float mechanism in a water tank.

III.  Links:

http://homeadvisor.msn.com/improve/plumbing.aspx

http://www.plumbnet.com/

http://www.plumbingweb.com/

http://www.theplumber.com/faq.html

http://www.theplumber.com/handbook.html

http://begin.com/fixit/

http://www.kohlerco.com/

http://www.hometips.com/

http://www.plumbingmart.com/

http://www.us.amstd.com/

http://www.masterplumbers.com/home.asp

http://www.hometime.com/projects/plmbelec.htm#plumbing

http://www.allabouthome.com/directories/dir_plumbing.html

http://www.howstuffworks.com/question89.htm

http://www.kasdansimonds.com/plumbing__mechanical___electri.html

http://www.lowes.com/lkn?action=howTo&p=Repair/makebathrepairs

http://www.lowes.com/lkn?action=howTo&p=Repair/RepBrkPipes

http://www.plumbingwarehouse.com/

http://www.lowes.com/lkn?action=categorySelect&category=Plumbing

Irrigation: http://www.lowes.com/lkn?action=howTo&p=LawnGarden/UndergroundSprinkler.html&topic=howToLibrary

http://www.worldhomecenter.com/dept/irrigation/FittingAcces/

http://jessstryker.com/

Toilets; http://www.howstuffworks.com/toilet.htm

http://www.howstuffworks.com/question504.htm

http://www.toiletology.com/index.shtml

http://www.hometime.com/projects/howto/plumbing/pc2plm7.htm

http://www.lowes.com/lkn?action=howTo&p=Repair/ToiletRep

http://www.stemdoctor.com/how_toilets_flush.htm

http://www.stemdoctor.com/installing_new_toilet.htm

http://www.stemdoctor.com/toilet_drainage_&_supply.htm

http://www.stemdoctor.com/toilet_repairs.htm

Sewer Systems: http://www.howstuffworks.com/sewer.htm

http://pipe.industrysearch.com/cgi/www/jump.plx?adid=5286&url=www%2eppfahome%2eorg%2f

http://www.tylerpipe.com/indexsp.htm

http://www.stemdoctor.com/drainage_&_supply.htm

Water Heater: http://www.howstuffworks.com/water-heater.htm

http://www.lowes.com/lkn?action=howTo&p=Improve/InstallWatHeater

http://www.lowes.com/lkn?action=howTo&p=Repair/WaterHtrMaintaince.html

Valves/shutoffs: http://www.hometime.com/projects/howto/plumbing/pc2plm4.htm

Bathroom: http://www.hometime.com/projects/howto/plumbing/pc2plm5.htm

http://www.stemdoctor.com/2_&_3_handle_bath_and_shower_faucet_repair.htm

Kitchen: http://www.hometime.com/projects/howto/plumbing/pc2plm6.htm

http://www.stemdoctor.com/replacing_drain_traps_and_pipes.htm

Repairing Faucets: http://www.hometime.com/projects/howto/plumbing/pc2plm8.htm

http://www.stemdoctor.com/single_control_faucet_repair.htm

http://www.stemdoctor.com/2_handle_bathroom_and_kitchen_faucet_repair.htm

http://www.stemdoctor.com/installing_faucets.htm

Unclogging Drains: http://www.hometime.com/projects/howto/plumbing/pc2plm9.htm

http://www.lowes.com/lkn?action=howTo&p=Improve/ClrDrains

Summary

Review the importance of maintaining the water system:

Replacing packing, o-rings, and washers in valves and faucets.

Repairing float valves and flush valves.

Evaluation

Students will be evaluated on their performance of repairing a faucet that leaks at the stem.

Students will be evaluated on their performance of repairing a dripping faucet.

Students will be evaluated on their performance of repairing a float mechanism in a water tank.

Individual Learning Activity

Lesson:	Plumbing Maintenance and Repair

Assignment:	Choose one of the topics below and research it. Write a report on your findings that answers the question or explains the concept and shows why it is relevant to your life.

1.	Replace worn or broken seals.

2.	Maintain pumping source.

3. 	Maintain control systems.

4.	Maintain drainage lines.

Minimum Requirements:

1. Paper must be typed in 12 point font and at least one page in length. The paper may be double-spaced.

2. At least two credible references must be properly cited.

3. All work must be original. No plagiarism! Any use of

another’s ideas without giving credit will result in a zero.

4. Papers will be graded on content (amount of good information, accuracy, etc.) and mechanics (grammar, spelling, and punctuation.)

Due Date:

Points/Grade Available:

Individual Learning Activity Rubric

| Content - offers current information on the topic chosen, thoroughly covers each aspect of the question, and demonstrates understanding and mastery of the lesson. The paper should include information and issues of state and local importance. | 35 pts. |
| --- | --- |
| Critical Analysis - logical process of analyzing and reporting information that examines and explains the topic selected. The paper should go beyond simply listing facts and must include why the concept is relevant to the student’s life. | 25 pts. |
| Organization- The paper should have an orderly structure that demonstrates a logical flow of ideas. | 15 pts. |
| Mechanics- spelling, grammar, punctuation, font size, double spacing, citation, etc. Essentially, the paper should meet all specifications and be executed following rules of proper written English. | 15 pts. |

Group Learning Activity

Lesson: 	Plumbing Maintenance and Repair

Assignment: 	Choose one of the topics below and research it. With your group, prepare a presentation to teach the class your concept.

1.	Replace worn or broken seals.

2.	Maintain pumping source.

3. 	Maintain control systems.

4.	Maintain drainage lines.

Your presentation should include the following:

- A lesson plan outlining exactly what your group will teach and how the information will be taught

- A Power Point of at least twelve slides

- Notes containing the information the class will be responsible for (these can be printed and given to the class, written on the board, or part of the Power Point). A copy of the notes will be turned in to the instructor.

- Some type of interactive activity for the class (game, problem solving activity, interactive model, etc.)

- Your group must also prepare an assessment for the class. This assessment can be written or oral, but should show the instructor that the class understands and has retained the material being taught.

Due Date:

Points/Grade Available:

All work must be original. No plagiarism! Any use of

another’s ideas without giving credit will result in a zero.

Group Learning Activity Rubric

| Lesson Plan – The group submits a thorough, detailed lesson plan highlighting the content and organization of their lesson. | 10 pts. |
| --- | --- |
| PowerPoint – The group presents a Power Point of at least twelve slides that contains information and pictures vital to the lesson with additional information or examples for enhancement. | 20 pts. |
| Interactive Activity – Some type of interactive activity is used to help teach the lesson. The activity should contribute to the mastery of content and involve the entire class in some way. | 15 pts. |
| Assessment – A fair, thorough assessment is prepared and administered based on the information presented to the class. Poor grades on the assessment by a few members of the class are excusable, but if the entire class has difficulty, the points awarded in this category may be lowered at the discretion of the instructor. | 15 pts. |
| Content – The group should cover the concept (within reason) in entirety. The group may study actual lesson plans to help decide what should be emphasized. | 25 pts. |
| Overall Effect – The group is prepared, enthusiastic, and interesting, and the lesson flows smoothly. | 15 pts. |

Presentation Learning Activity

Lesson:	Plumbing Maintenance and Repair

Assignment:	Choose one of the topics below, research it, and prepare a presentation that answers the question or explains the concept and shows why it is relevant to your life.

1.	Replace worn or broken seals.

2.	Maintain pumping source.

3. 	Maintain control systems.

4.	Maintain drainage lines.

Minimum Requirements:

Oral Report Option

1.   Write a paper on one of the topics and orally present your work to the class.

2.   Paper may be double-spaced and should be at least one page in length, resulting in a two to five minute presentation.

3.   At least two references must be properly cited.

4.   The presentation of the report will be graded secondary

to the content of the paper.

PowerPoint Option

- Presentation should be at least ten slides in length

- Presentation should include at least four photos.

- Presentation should be two to five minutes in length.

- Grammar and spelling will be graded by the same standards as any other written assignment.

- At least two references must be properly cited.

Poster Option:

- Prepare a poster that answers/explains one of the topics. You will present your poster to the class.

- Your poster should include both text and graphics that help communicate your research.

- At least two sources of information should be properly cited on the back of the poster.

- Neatness and appearance of the poster will be graded.

- Poster presentation should last two to five minutes.

Due Date:

Points/Grade Available:

For all presentations: All work must be original. No plagiarism! Any use of another’s work or ideas without giving proper credit will result in a zero.

Presentation Learning Activity Rubric

| Content- offers current information on the topic chosen, thoroughly covers each aspect of the question, and demonstrates understanding and mastery of the lesson. The presentation should include information and issues of state and local importance. | 40 pts. |
| --- | --- |
| Critical Analysis/Organization – The presentation shows a logical process of analyzing and reporting information that examines and explains the topic selected. The presentation should go beyond simply listing facts and must include why the concept is relevant to the student’s life. | 20 pts. |
| Presentation – The student makes a genuine effort to present, not just read the material. The student should present with confidence using techniques like eye contact and voice inflexion to make his or her point. Although content takes precedence over presentation, the experience of successfully presenting in front of a class is part of the basis of this assignment. | 25 pts. |
| Mechanics- spelling, grammar, punctuation, font size, double spacing, citation, etc. Essentially, the presentation should meet all guidelines set forth and should be executed in proper written English. For the poster, this includes neatness and appearance. | 15 pts. |

Essential Question:

How do you maintain and repair plumbing?

Vocabulary

Faucet

Valve